## Slide 1
MODELLING OF BAITARANI SUB-BASIN USING RIVER SYSTEM APPROACH THROUGH SOURCE SOFTWARE
BASIN PLANNING & MANAGEMENT ORGANISATION, CENTRAL WATER COMMISSION
MINISTRY OF WR,RD & GR
GOVERNMENT OF INDIA

## Slide 2
ELEVATION

## Slide 3
Total area: 14,218 km2
Odisha- 13,482 km2 (94.83%),
Jharkhand- 736 km2(5.17%)
Modelled area of 6 sub-catchments 10,363 km2
15% Urban population
Objectives

## Slide 5: Multiple Issues of Multiple Stakeholders
Water Harvesting
Catchment Degradation
Water Pollution
(Waste Dumps, Industries,
Domestic, Fertilizer/Pesticide)
Lift/Canal/GW Irrigated Agriculture
Competing Water Uses
Water Scarcity
GW Management
WUA/ Farmers
Water Res Dept
Agriculture Dept
Forest Dept
Industry/Mining Dept
Livestock & Fisheries Dept
Env. dept
Urban & Rural Water Supply & Sewerage
Baitarani Sub-Basin

## Slide 6
E_Flow:
20% in Monsoon(Jun-Oct), 25% in Non-Monsoon(Nov-Feb), 30% in Lean(Mar-May)
Total annual = 1158 MCM
(% of Average flow)

## Slide 7: Irrigation in Major, Medium, Minor & Lift Irrg Projects & Rainfed areas
Chart: Irrigated Area (Th Ha)
| 2015 | 2021 | 2051
Maj & Med (Modelled)(Th Ha) | 150.79 | 208.094 | 448.307
Minor & Lift (Estimated) | 122.7 | 130.876 | 171.3
Rain-fed | 221.465 | 130.661
Key issues

## Slide 9
Water Availability vrs demand (MCM) in sub-basin
Chart: Water Allocation & Unutilized Flow in 2015
| Dom/Liv | Irrigation | Industry | E Flow | Unutilized Flow
2015 | 106 | 563.62 | 43.8134 | 1158.32 | 3770.2466
Chart: Water Allocation & Unutilized Flow in 2021
| Dom/Liv | Irrigation | Industry | E Flow | Unutilized Flow
2021 | 136 | 783.18 | 228.959 | 1158.32 | 3335.541
Chart: Water Allocation & Unutilized Flow in 2051
| Dom/Liv | Irrigation | Industry | E Flow | Unutilized Flow
2051 | 315 | 2632.45 | 284.959 | 1158.32 | 1251.271
Demand

## Slide 10
Average Annual SW availability & in 75% dependable year

## Slide 11
Chart: Growth of Demand (in time) versus Water Availability Baitarani basin
| 2015 | 2021 | 2051
Demand | 2404.7534 | 2899.459 | 5282.729
Average Availability (5642) | 5642 | 5642 | 5642
75% Dependable Availability (4097) | 4097 | 4097 | 4097
CC Dry- Average Availability (4939) | 4939 | 4939 | 4939
CC Dry- 75% Dependable Availability (3337) | 3337 | 3337 | 3337

## Slide 12
Chart: Demand (in time) vrs Water Availability (Champua)
| 2015 | 2021 | 2051
Demand | 154 | 424 | 606
Average Availability (467) | 466.6 | 466.6 | 466.6
75% Dependable Availability (280) | 279.5 | 279.5 | 279.5
CC Dry- Average Availability (412) | 412 | 412 | 412
CC Dry- 75% Dependable Availability (229) | 229 | 229 | 229

## Slide 13
Command Areas – Existing, Ongoing, Proposed Major & Medium Projects
110 Th Ha (2015)
144 Th Ha (2021)
313 Th Ha
(2051)

## Slide 15: Key Findings
Proposed projects will even out flooding in monsoon & drying of river in lean season due to spatio-temporal variation of RF & increase the utilisability of water in the sub-basin
Coming up of large no of industries would create water stress in Upper parts of sub-basin (Champua) in 2051 as total water use (606 MCM) overrides average availability (467 MCM). The water stress enhances further in Dry_CC scenario as water availability reduces to 412 MCM.
Sound water budgeting for industry, agriculture in especially Champua, Anandpur and Akhuapada sub-catchments can trade-off water demand to a considerable extent.
Under climate change, wet years are expected to be wetter & dry years are expected to become drier. In order to combat the challenges of possible climate change effects on water resources availability, ET and crop productivity, it is suggested to speed-up the creation of new water storage mechanism. So, there is need to store water available in wet years in appropriate sized storages, including groundwater for later use in drier months.
E-Flows need to be determined in various reaches based on the evidence-based EIA studies.

## Slide 16: Key Findings……
After development in 2051, sub-basin is expected to have water surplus of about 1250 MCM
Under CC_Dry scenario (2051), if about 1000 MCM is met from GW & 10% enhancement of irrigation WUE may alleviate shortages
Lessons learned
Water productivity remain very low due to lack of maintenance of the infrastructure, inappropriate delivery services & users low awareness leading to substantial wastage