## Slide 1
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Prioritising soil conservation and water quality issues for the Waikato River and Waipā River Restoration Strategy, New Zealand.
Reece Hill1,2, Dan Borman1,2 and Tane Desmond1
1 Waikato Regional Council
2 Landsystems Limited

## Slide 2
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
About the Restoration Strategy
The Restoration Strategy covers the Waikato and Waipā River Catchments as defined by several Treaty of Waitangi Iwi Settlement Acts.
Through the Treaty settlements, around $6m NZD are available annually to fund river related improvements in the Waikato and Waipā River Catchments.
The Restoration Strategy will guide the funding of projects to ensure they address priority areas and issues.
This presentation focusses on the science component of the strategy that identifies priority areas for addressing land based issues and the impact of mitigations.

## Slide 3
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Overview
Science contribution
Methods – the GIS framework
Results and findings
Lessons learned

## Slide 4
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Science contribution
To develop an easy to interpret spatial approach and outputs for identifying and prioritising soil conservation issues across sub-catchments.
The information will inform the restoration strategy process.
Including:
  Where soil conservation issues are greatest.
  The range of mitigations being used on the ground.
  Where mitigations can be placed.
  An estimate of the cost for mitigations by sub-catchment.
  An estimate of likely the sediment reductions if mitigations are implemented.

## Slide 5
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Science contribution
Based on previously developed GIS-based framework
Using available model data
  Erosion and sediment generation
  Land use intensity
  Vegetation cover
A broader approach
  Land focussed – mitigate the issues on the land
  A relative picture across sub-catchments
  Hydrologically connected and scalable
  Getting the best from different models

## Slide 6
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Hillslope erosion and sediment model data
Streambank erosion and sediment model data
Landuse and landcover model data
Issues – multiple model data and ranking
Stabilise landslides on pasture
Plantation forests on pasture
Retire pasture
Sediment traps
Riparian planting
Riparian fencing
Mitigations – spatially match issues
Mitigation costs and sediment reductions
Estimates – spatially match mitigations

## Slide 7
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Hillslope erosion and sediment model data
Streambank erosion and sediment model data
Landuse and landcover model data
Issues
Multiple model data was normalised to combine
Watershed scores - area weighted lengths and areas of issues.
Sub-catchment scores – sum of watershed scores weighted by sub-catchment area
Sub-catchments ranked by issue scores

## Slide 8
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Issues – Upper Waikato sub-catchment sediment

## Slide 9
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Ranking sub-catchments issues

## Slide 10
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Ranking sub-catchments issues

## Slide 11
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Mitigations varied across the Waikato catchment.
Reality tested with land management staff workshops.
Specific mitigations imposed on the land identified as having issues.
Stabilise landslides on pasture
Plantation forests on pasture
Retire pasture
Sediment traps
Riparian planting
Riparian fencing
Mitigations

## Slide 12
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Mitigation – streambank example

## Slide 13
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Mitigation – streambank example
Fencing completed

## Slide 14
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Mitigation – streambank example
Fencing required
Planting required

## Slide 15
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Mitigation – streambank example
Costs

## Slide 16
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Cost estimates aggregated for sub-catchments.
Sediment reduction estimates for each mitigation were imposed on watersheds and aggregated for sub-catchments.
Available literature was used to estimate reductions.
A range of maps, graphs and data tables was useful to show the estimates across the sub-catchments.
Mitigation costs and sediment reductions
Estimates

## Slide 17
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Whirinaki sub-catchment | Estimates |  |  | 
 | Mitigation cost | Sediment reduction | Sediment reduction | Reduction cost / ton
Hillslope | $20.8 m | 52% | 2325 t/yr | $9000/t
Streambank | $2.2 m | 8% | 320 t/yr | $6900/t
Total | $23.0 m | 19% | 2645 t/yr | $8700/t

## Slide 18
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Reductions (t/yr)
Costs ($)
Reductions (%)
Upper Waikato sub-catchments - hillslope sediment

## Slide 19
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Reductions (t/yr)
Costs ($)
Reductions (%)
Upper Waikato sub-catchments - streambank sediment

## Slide 20
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Application success
A range of model derived spatial data were combined in a meaningful way to inform the restoration strategy.
Provided a clear and realistic overview of relative sub-catchment land related issues, estimates of mitigation costs, and likely sediment reductions.
The visual and spatial outputs were well received by a wide ranging audience.
The approach was very flexible and could be updated in quick response to requested changes.

## Slide 21
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Lessons learned
Science information from multiple models can be made accessible to a broad audience.
A spatial and visual approach assisted information uptake.
Compromises are required for the GIS based mitigations.
Science was essential but one of many consideration when prioritising sub-catchments for funding.
Iterative process and full involvement of “on-the-ground” land managers was an essential requirement for success.

## Slide 22
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Acknowledgements
My Co-authors.
Technical Advisory Group members.
Waikato Regional Council and DairyNZ.
Restoration Strategy team at Envirostrat.
The INFFER team.
Landsystems Limited for funding my attendance.
Thank you