## Slide 1: ASSESSMENT OF ENVIRONMENTAL FLOWS FOR THE TAPI RIVER BASIN, INDIA
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
P. V. Timbadiya, Ph.D.
Assistant Professor in Water Resources Engineering
Department of Civil Engineering
S. V. National Institute of Technology – Surat, Gujarat, India

## Slide 2: Outline of the presentation
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Introduction
Study Area and Data Collection
Methodology
Results and Discussion
Conclusions

## Slide 3: Introduction
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Water is generally used for diverse purposes such as irrigation, power generation, drinking and sanitation and industrial use.
The assessment of water requirements of freshwater-dependent ecosystems is a challenging task considering the complexity of the physical processes and interactions between the components of the ecosystem (Smakhtin and Anputhas, 2006)
Environmental requirements of the rivers are defined as a suite of flow discharges of certain magnitude, timing, frequency and duration.
These flows ensure a flow regime capable of sustaining a complex set of aquatic habitats and ecosystem processes and are often referred as ‘environmental flows’ or ‘environmental water requirements’.

## Slide 4: Introduction
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Environmental flow (EF) plays important role in protecting bio-diversity.
In the developing country such as India estimation of EF is still at primary level.
India faces numerous water related challenges including increasing water shortages and competing water demand between different sectors and states.
Vast spatio-temporal variability of monsoon is another challenge.
The National River Linking Project (NRLP) has been proposed by Government of India which envisages transferring the water from the river basins of North & East viz., Ganga, Brahmaputra and Meghna to the basins of South & West.

## Slide 5: Introduction
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Spatial variation in mean annual precipitation across India ranges from about 100 mm in western Rajasthan to more than 2500 mm in Northeastern region to a maximum of 11,000 mm near Cherrapunji.
Source: commons.wikimedia.org

## Slide 6: Introduction
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
The major flood prone regions are Punjab, Haryana, most of the Gangetic plains including Uttar Pradesh, North Bihar and West Bengal, the Brahmaputra valley, coastal Andhra Pradesh and Orissa, and South Gujarat.
Source: nihroorkee.gov.in

## Slide 7: Introduction
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Source: indiawaterportal.org
Success ????
15 major river
45 medium
120 minor
Number of ephemeral streams

## Slide 8: Introduction
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
The National Commission for Integrated Water Resources Development Plan project 2% of the total national water requirement as EF.
It is estimated as 10 km3 and 20 km3 for year 2025 and 2050 without specifying its geographical location and any scientific basis.
Also, basin specific study on EF has not been carried out yest except for Brahmaputra basin.
The initial estimate of Environment Flow for the Tapi River has been estimated.

## Slide 9: Study Area and Data Collection
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Tapi River Basin
Area: 65,145 km2
Mean annual runoff: 14.9 BMC
Tapi River length: 724 km
Minor, Medium and Major Hydraulic Structures on Tapi River

## Slide 10: Study Area and Data Collection
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Hydro observation sites on Tapi River
Dedtalai
Burhanpur
Bhusaval
Gidhade
Savkheda
Sarangkheda
Ghala
Hydro observation sites on Tapi River

## Slide 11: Methodology
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Detailed assessment based on primarily holistic approach
Rapid assessment based on analysis of hydrological time series.
The global flow environmental flow calculator developed by IWMI, Sri Lanka and Water System Analysis Group of University of Hampshire, USA which is based on natural hydrological variability.
Observed flow data converted to monthly flow data at particular gauging station to compute actual mean annual runoff (MAR).
Flow duration curve for entire range of probabilities of occurrence has been computed.

## Slide 12: Environmental Management Classes (EMC)
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Classes A & B
Unmodified and largely natural conditions
Where no or limited modification is present
Class C
Modified river ecosystems
The modifications are such that they generally have not affected the ecosystem integrity
Class D
Largely modified ecosystems
Considerable modification from the natural state where the sensitive biota is reduced in number and extent
Classes E & F
Seriously and critically modified ecosystems
Most ecosystem’s functions and services are lost

## Slide 13: Results and Discussions
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Burhanpur

## Slide 14: Results and Discussions
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Burhanpur
Flow Duration Curves with EMC

## Slide 15: Results and Discussions
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Savkheda

## Slide 16: Results and Discussions
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Savkheda
Flow Duration Curves with EMC

## Slide 17: Results and Discussions
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Sarangkheda

## Slide 18: Results and Discussions
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Sarangkheda
Flow Duration Curves with EMC

## Slide 19: Eutrophication in Tapi River
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY

## Slide 20: Conclusions
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Actual mean annual runoff at Burhanpur, Savkheda and Saragkheda is 4317, 8043 and 8404 MCM.
Required MAR for natural management of the Tapi river is 50.1%, 52.2% and 56.1 % of actual MAR respectively Burhanpur, Savkheda and Saragkheda station.
If MAR fall below 0.7%, 1.6% and 1.4% of actual MAR respectively Burhanpur, Savkheda and Saragkheda station, then river will reach to the critically modified state at that location and hence, total natual habitant and biota will lost.

## Slide 21: Acknowledgment
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Centre of Excellence on Water Resources and Flood Management at SVNIT Surat for providing data and other support

## Slide 22
BRISBANE, AUSTRALIA | 18 - 20 SEPTEMBER 2017
MANAGED BY
Thank You