## Slide 1
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Novel evapotranspiration model to inform future water management using past riparian vegetation trends
Tanya Doody, Micah Davies, Garth Warren, Martin Nolan
15th October, 2018

## Slide 2
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Biodiversity
Ecological targets and objectives (e.g. maintain 70% of Red Gum in good health)
Mechanism - monitoring and environmental flow allocations
Murray-Darling Basin

## Slide 3
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Decision context
Water for irrigation, human consumption and environment
Key tree species, condition cycles, water requirements
River Cooba

## Slide 4
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Tree condition surveys – seasonal at best, labour intensive
Remote sensing tool required to support decision making (temporal)
Prioritising environmental flow allocations

## Slide 5
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Field quantification of tree water use
Evapotranspiration (ETa) = transpiration + interception + soil evaporation
Site | Rainfall (mm) | Interception (mm) | Evaporation (mm) | Transpiration (mm) | ET (mm)
1-2yr | 422 | 42(±3) | 246(±57) | 566 (± 394) | 854 (± 394)
2-2yr | 422 | 42(±3) | 246(±57) | 392 (± 117) | 680 (± 117)
1-5yr | 395 | 17(±3) | 219(±46) | 84 (± 49) | 320 (± 49)
2-5yr | 405 | 29(±3) | 250(±73) | 208 (± 127) | 487 (± 127)
1-10yr | 396 | 18(±3) | 264(±59) | 17 (± 3) | 299 (± 3)
1:2 mean ETa = 767 mm year-1
1:5 mean ETa = 404 mm year-1
Potential threshold of >550 mm year-1
770
400
Doody TM, Colloff MJ, Davies M, Koul V, Benyon RG, Nagler PL. 2015. Quantifying water requirements of riparian river red gum (Eucalyptus camaldulensis) in the Murray-Darling Basin, Australia –implications for the management of environmental flows. Ecohydrology. 8(8), 1471-1487.

## Slide 6
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Development of CSIRO-FETa
Produce 8-day, 250m resolution CMRSET product – national ET layer
Validation with field ETa = CSIRO FETa
CMRSET * (CSIRO MODIS Reflectance Scaling of ETa)
Vegetation greenness (EVI) - transpiration and interception
Surface wetness (residual Moisture Index RMI) - evaporation
Interpolated climate data (Priestley-Taylor PET and precipitation)
*CMRSET (Guerschman et al., 2009)

## Slide 7
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
CSIRO-FETa

## Slide 8
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Case study – Yanga National Park Red Gum
> 3 years below threshold

## Slide 9
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Case study – Gol Gol wetland Red Gum
> 3 years below threshold
No response of river trees to flood (max ETa)
Rapid decline of trees to previous state

## Slide 10
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Management implications
Simple tool to observe past trends in vegetation response to flood and drought
Temporal resolution – monthly, annually, 2001-current
Mangers can compare past responses, with inundation and rainfall history and future climate projections to base e-flow decisions
Identify high priority areas for future e-flow allocations
Provide improved estimates of floodplain vegetation for water accounting purposes

## Slide 11
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
CSIRO-FETa provides a tool to help water managers ensure that floodplains cycle through wet and dry periods to maintain ecosystems function and biodiversity
Conclusion

## Slide 12
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
CSIRO
Richard Benyon
Matt Colloff
Micah Davies
John Lamour
Pamela Nagler
Jodie Pritchard
Leroy Stewart
Dale Worledge
Funidng: CSIRO
NSW Office of Environment and Heritage
James Maguire
Paul Childs
Aknowledgements

## Slide 13
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY
Thank you
CSIRO Land and Water
  Dr Tanya Doody Spatial Ecohydrologist
    t +61 8 8303 8716
    e tanya.doody@csiro.au
https://research.csiro.au/mwe/

## Slide 14
SYDNEY, AUSTRALIA | 14 -18 October 2018
MANAGED BY